## Slide 1: Extracellular Vesicles as Drug Carriers: Establishing a Loading Protocol and Prototyping a Microfluidic Chip
Simon Ignjatovic – University of Georgia
Mentor: Jessica Ayivi
Principal Investigator: Dr. Kristen Dellinger

## Slide 2: Extracellular Vesicles (EVs)
Lipid bilayer-delimited nanoparticles
Range from 10-20 nm to 10 micron in diameter [1]
Naturally produced by cells containing source cell biomarkers
Vital to cell-to-cell communication
Research interests:
  Tumor targeting
  Disease identification
  Drug delivery
Stago.com [1]
1
Notes: Highlight drug delivery

## Slide 3: Loading Methods
Int J Nanomedicine, 2020, 15, 6485-6502 [2]
2
Notes: Call attention to endogenous (pre-isolation) vs exogeneous (post-isolation) and active vs passive loading  focus passive

## Slide 4: Microfluidic Loading
Lab Chip, 2025, 25, 1718-1727. [4]
Small, 2021, 17, 2102150. [3]
3
Notes: Mention Need for standardized studies to segway into next slide

## Slide 5
Mentor’s aim:
Aim 1: Establish a Reproducible Workflow for Fluorescent Cargo Loading and Baseline Release Characterization Across EV Subpopulations
My aims:
Aim 1: Develop a Protocol for Passive Loading of Fluorescent Cargo in EVs
Aim 2: Develop a Microfluidic Chip for Fluorescent Cargo Loading of EVs
4

## Slide 6: Aim 1: Passive Loading
Passive loading with Calcein
  Hydrophilic fluorescent dye
  Capable of self-quenching above 70 mM
EVs isolated from human prostate cancer (PC-3) and human embryonic kidney (HEK) cell lines
EV isolation using size exclusion chromatography (SEC) with Izon qEVoriginal 500 µL column
Pubchem [5]
Figure 1: PC-3 cells.
5

## Slide 7: Aim 1: Passive Loading
Incubation at 37°C for 24 hours
3 test trials:
  Trial 1: 200 µL 3.06 x 108 EVs + 300 µL 4 mM calcein
  Trial 2: 200 µL 3.06 x 108 EVs + 300 µL 5 mM calcein
  Trial 3: 200 µL 3.06 x 108 EVs + 300 µL 2.5 mM calcein
Wash solution of free calcein via SEC
Measure fluorescence before and after lysing with Triton X-100 (Biotek Cytation5 image reader)
Measure size distribution and concentration before and after loading (Malvern NanoSight Pro)
Pubchem [5]
Figure 2: HEK cells.
6

## Slide 8
Figure 3: Fluorescence results of Loading Test 1 with PC-3 cells
Figure 4: Fluorescence results of Loading Test 2 with HEK cells
Aim 1: Results
7

## Slide 9
Figure 5: Fluorescence results of Loading Test 3 with HEK cells
Aim 1: Results
 | P-values
Loading Test 1 | 5.3 x 10-13
Loading Test 2 | 2.77 x 10-07
Loading Test 3 | 1.46 x 10-16
Table 1: Results of two-way ANOVA tests across EVs and Trials.
8

## Slide 10: Aim 1: Results
Figure 6: Size distribution and concentration of PC-3 EVs before loading.
Figure 7: Size distribution and concentration of PC-3 EVs after loading.
9

## Slide 11: Aim 1: Results
Table 2: Post-lysing EE%. All values are percents.
10

## Slide 12: Aim 2: Microfluidic Device
1. 3D model mold
2. 3D print mold
3. Cast mold with PDMS
11

## Slide 13: Aim 2: Microfluidic Device
4. Punch holes and plasma bond PDMS to glass slide
5. Leakage test of finished device.
12

## Slide 14: Aim 2: Design
Figure 8: Microscope image of herringbone.
Figure 9: Dimensioned 3D print model. All units in mm.
13

## Slide 15: Conclusions
Aim 1:
Successfully loaded EVs with fluorescent calcein by passive incubation
Moving forward:
  Use standardized EV : calcein molar ratios
  Explore calcein self-quenching concentrations
Aim 2:
Successfully developed a microfluidic device
Moving forward:
  Test device with EV & calcein solution
14

## Slide 16: Acknowledgements
Thank you to Dr. Kristen Dellinger, Jessica Ayivi, and Gregory Roberts for their continuous support and guidance
Work funded by NSF REU Award No. 2349519 and NSF Award No. 2302452
Thank you to the Nanobio Innovations Lab, the Joint School of Nanoscience and Nanoengineering, North Carolina A&T University, and the University of North Carolina Greensboro
15

## Slide 17: References
[1] “Extracellular Vesicles (EVs) – Microvesicles (MVs) | Stago.com,” 2024. Accessed: July 23, 2026. [Online]. Available: https://www.stago.com/haemostasis/tests-clinical- applications/extracellular-vesicles-evs-microvesicles-mvs/
[2] T. Huyan et al., “Extracellular Vesicles – Advanced Nanocarriers in Cancer Therapy: Progress and Achievements,” International Journal of Nanomedicine, vol. Volume 15, pp. 6485–6502, Aug. 2020, doi: 10.2147/ijn.s238099.
[3] R. Hao, Z. Yu, J. Du, S. Hu, C. Yuan, H. Guo, Y. Zhang, H. Yang 2102150, A High -Throughput Nanofluidic Device for Exosome Nanoporation to Develop Cargo Delivery Vehicles. Small 2021, 17, 2102150. https://doi.org/10.1002/smll.202102150
[4] C. Piunti, S. Micheli, S. Giancaterino, P. Fusco, C. Boi, and E. Cimetta, “Microfluidic loading of verteporfin into extracellular vesicles for neuroblastoma therapy,” Lab on a Chip, vol. 25, no. 7, pp. 1718–1727, 2025, doi: https://doi.org/10.1039/d4lc01103a.
[5] PubChem, “Calcein,” PubChem, 2026. Accessed: July 23, 2026.[Online]. Available: https://pubchem.ncbi.nlm.nih.gov/compound/Calcein
16