## Slide 1: Advanced Packaging Validation Technology
PI: Dr. Seung Joon Paik, Dr. Yogendra Joshi
Mentor: Junyoung Kim
REU: Nathan Pak
Notes: Add more numbers, graphs, fancy

## Slide 2: What is Packaging?
  The structure supporting a die
    Protects the die from drops, corrosion, static electricity, etc.
    The connections around a die
    Allows the chip to be integrated into a printed circuit board (PCB)
Silicon Wafer
Notes: What is a die, how is it made, how we can interact with it, end user

## Slide 3: What is Advanced Packaging?
Combining multiple chiplets into one package, rather than one large chip
Decreases latency
  Shorter travel distances, more connections
More efficient method of manufacture
  Whole chip does not rely on one defect

## Slide 4: Advanced Packaging Applications
Nvidia announced Vera Rubin at Computex 2026
Can power agentic artificial intelligence (AI)
Utilizes High Bandwidth Memory (HBM), which relies on advanced packaging

## Slide 5: What is Validation Technology?
Validate connections within the package
Non-Destructive Validation Technology
  Previously relied on cross section analysis and KGD (known good die) and other limited techniques
    Methods such as acoustic microscopy, X-ray tomography, etc.
Notes: Chip might work, reliability unsure bad

## Slide 6: Test Vehicle Fabrication
Single chip structure (monolithic)
Utilizes daisy chaining to emphasize defects
Uses MB50 test die (50 micron pitch)
Single Coupon
17mm
50um
MB50
Notes: What is a coupon, add scale to pictures, and in zoomed image spacing, try adding title under image

## Slide 7: Process
SiO2
Silicon
SiO2
(a) Cleaning & Oxidation
(b) Seed Layer Deposition
Ti/Cu
SiO2
Ti/Cu
Silicon
Silicon
(c) Photolithography
PR
SiO2
Ti/Cu
Silicon
(d) Cu Electroplating
Cu
SiO2
Ti/Cu
Silicon
(e) Surface Finish
Ni
Au
SiO2
Ti/Cu
Silicon
(f) PR Liftoff
SiO2
Silicon
(g) Seed Layer Etching
SiO2
Silicon
(h) Solder Mask Coating
Solder Mask (Dryfilm)
SiO2
Silicon
(i) Lithography and Dicing
SiO2
Silicon
(j) Flip Chip Bonding
Underfill
MB50
Notes: I’ve been working on highlighted parts

## Slide 8: My Contributions
Oxidation
  Create a dielectric seed layer to prevent electrical interaction with silicon
Photolithography
  Deposit a pattern for electrical paths
Metallization
  Create adhesion layers between silicon oxide and copper paths
  Deposit a corrosion resistant surface finish
SiO2
Silicon
SiO2
(a) Cleaning & Oxidation
(b) Seed Layer Deposition
Ti/Cu
SiO2
Ti/Cu
Silicon
Silicon
(c) Photolithography
PR
SiO2
Ti/Cu
Silicon
(e) Surface Finish
Ni
Au
SiO2
Ti/Cu
Silicon
(f) PR Liftoff

## Slide 9: Current Progress
Silicon wafers oxidized (2 micron) and seed layer deposited (1.5 micron)
Notes: Add more details with what I did about this

## Slide 10: Current Progress
Wafer photoresist coated
  SPR220 at 1000RPM for 40 seconds
  Recipe edited for edge bead removal at 4000RPM for 1 second
  Thinner than needed for process (>14 um), at 10-11 um

## Slide 11: Current Progress
Exposed and developed, next step is electroplating

## Slide 12: Current Progress
Surface finish tests
Nickel (3000A) and gold (1000A)

## Slide 13: Current Progress
Surface finish tests
Titanium (200A), nickel (3000A), and gold (1000A)

## Slide 14: Current Progress
Surface finish tests
Titanium (200A) , and gold (1000A)

## Slide 15: Finished Coupon Inspection
Coupon surface finish inspected
  Attempt to predict defects
  Each coupon measured in 8 sections
1 2
5 6
3
4
7
8
Notes: What is a coupon, how it differs from die

## Slide 16: Finished Coupon Inspection
Most recent processed wafer
  No more surface texture issues
  Surface finish peeling issues

## Slide 17: Next Steps
Bonding tests for hybrid bonding
  Skips solder bumps to allow denser connections (<1 um)
  Bonds dielectric material first, then metals
  Next step in packaging research
Notes: Explain how this connects with the project, the dieletric is the oxide

## Slide 18: Next Steps
Wafers with oxide and nitride layers for bonding tests
SiO₂ #1
SiO₂ #2
SiO₂ #3

## Slide 19: Closing Remarks
Contributions
  Processing back up and experimental wafers
  Surface finish testing and liftoff
Advanced packaging research used for chip manufacturers
  Ensure reliability for every unit
Test vehicles fabricated to experiment with inspection methods
Current fabrication issues
  Surface finish
  Photoresist edge bead

## Slide 20: Acknowledgement
Internship Coordinators
Leslie O’Neill
Dr. Mikkel Thomas
Research Project Members
Dr. Seung Joon Paik
Dr. Yogendra Joshi
Dr. Kyoung-Sik Moon
Junyoung Kim
Matthew Kim
Cleanroom Staff
Milette Handley
Vickiana Rosefort
Gary Spinner
Charlie Turgeon
Christopher White

## Slide 21: Questions?
Notes: Longer, don’t rush